## Slide 2: Schedule
BONUS
LIGHTING IoT PROJECT
USING PHOTOVOLTAIC ENERGY
INTRODUCTION TO MICROCONTROLLERS
What are microcontrollers ?
Main uses, detailing, which to use…
Differences between some microcontrollers
Differences between Arduino UNO, ESP32 and Raspberry PI
ARDUINO
Creation;
Arduino Uno detailing
Multimeter, wire gauge and project.
Show multimeter usage;
How to calculate the Wiring Gauge to be used;
Battery association + Project.
2022 Lenovo Internal. All rights reserved.

## Slide 3
A microcontroller is a single integrated circuit chip that contains a processor core, memory, and programmable input and output peripherals.
WHAT ARE MICROCONTROLLERS?

## Slide 4
Automation of various systems;
Brightness control;
Timers;
Sensor reading;
The usability is huge!
MAIN USES

## Slide 5
WHAT TO CHECK BEFORE LEAVING USING A MICROCONTROLLER?
Datasheet;
Web forums;
Developer channels;
Web Search;

## Slide 6
WHICH MICROCONTROLLER TO USE IN THE PROJECT ?
Computing power
Voltage and amperage
Versatility
Final cost
Between others...

## Slide 7
Computing power
MAIN DIFFERENCES BETWEEN ARDUINO, RASPBERRY PI AND ESP32
  Arduino UNO
  2005
  R$112,00
  Raspberry PI 3
  2012 - 2016
  R$1249,00
  ESP 32 2016
  R$75,90
Voltage and amperage
Versatility
Final cost

## Slide 8
SUMMARY OF THE DIFFERENCES BETWEEN ARDUINO, RASPBERRY PI AND ESP32
 | ARDUINO UNO | ESP32 | RASPBERRY PI 3
A | 40mA | 220mA | 1200mA
Clock | 8 bits | 32 bits | 1.2 GHz 64 bits
Bluetooth | NO | 4.0 | 4.1
Wi-Fi | NO | YES | YES
RAM | 2Kb | 520Kb | 1Gb

## Slide 9
ARDUINO MICROCONTROLLER OVERVIEW
Creation;
Board configuration;
IDE download and installation
See this microcontroller in more detail

## Slide 10
ARDUINO CREATION
Basic stamp
Wiring-Blink

## Slide 11
ARDUINO CREATION
Arduino-USB-v2
Arduino UNO

## Slide 12
MORE ABOUT THE ARDUINO MICROCONTROLLER

## Slide 13
HOW TO INSTALL AND CONFIGURE ARDUINO FOR FREE
https://www.arduino.cc/en/software
http://www.wch-ic.com/downloads/CH341SER_EXE.html
Page to download the Arduino IDE
Page suggestion to download the serial communication driver

## Slide 14
MULTIMETER
Multimeters are electronic equipment capable of measuring various electrical quantities such as voltage, current, resistance, capacitance, continuity, etc.
The sensitivity and number of functions of a multimeter can greatly influence the value of the equipment.

## Slide 15
EXAMPLES OF MULTIMETERS
~R$26,00
~R$7800,00

## Slide 16
HOW TO KNOW THE CIRCUIT AMPERAGE?
Single Phase / Biphasic
I = P / U
I = P / U x FP
Or
* Recommended
I = P / U x 1.15
COPPER CABLES | 
METRIC STANDARD | 
ABNT NBR 5410 | 
SECTION (mm²) | MAX. AMPERAGE
0.5 | 6 A
0.75 | 10 A
1 | 12 A
1.5 | 15.5 A
2.5 | 21 A
4 | 28 A
6 | 36 A
10 | 50 A
16 | 68 A
25 | 89 A
35 | 111 A
50 | 134 A
70 | 171 A
95 | 207 A

## Slide 17
MAXIMUM VOLTAGE AND ELECTRICAL CURRENT THAT THE BODY CAN HANDLE
I = P / U

## Slide 18
MAXIMUM VOLTAGE AND ELECTRICAL CURRENT THAT THE BODY CAN HANDLE
I = P / U = 100W / 110V = 0,90A = 900mA
1 mA = Body is able to feel
From 9 mA = Slightly painful process
From 9 to 20 mA = In addition to pain, the person loses part of muscle control and is unable to let go of the electrical conductor.
*** Above that, the problems become more serious, and can cause death.
75 mA = The electrical discharge begins to interfere with the heart, which also works with an electrical mechanism, causing a cardiac arrhythmia.

## Slide 19
PROJECT
Lighting IoT project using photovoltaic energy.
Photovoltaic solar panel
Lithium battery charger – CN3065
Battery
Voltage regulator - Lm2596
Arduino Uno
Ethernet shild W5100
Led
Lamp

## Slide 20
CONNECTING BATTERIES IN SERIES AND PARALLEL
PARALLEL
SERIES
Voltage = sum of each battery voltage
Electric current = keep the same

## Slide 21
.com
KEY PRECAUTIONS WHEN WORKING WITH MICROCONTROLLERS
Always look for a qualified professional to work with electrical currents;
Always observe the supply voltage, working voltage, output voltage as well as the amperage of each component to be used;
Always check the technical specifications of microcontrollers
Draw or sketch the schematic
of the project before you go
shopping for parts.
Notes: You can safely remove this slide. This slide was provided by PoweredTemplate.com – You can download more templates, shapes and diagrams for presentations from https://poweredtemplate.com

## Slide 23
BIBLIOGRAPHY
MAXIMUM VOLTAGE AND ELECTRICAL CURRENT THAT THE BODY CAN HANDLE
https://super.abril.com.br/ciencia/que-voltagem-maxima-um-ser-humano-suporta/#:~:text=De%209%20a%2020%20miliamp%C3%A8res,provocando%20defici%C3%AAncia%20do%20sistema%20respirat%C3%B3rio
ARDUINO UNO R3 DATASHEET
https://docs.arduino.cc/hardware/uno-rev3
ESP32 DATASHEET
https://www.espressif.com/en/support/documents/technical-documents
DATASHEET RASPBERRY
https://datasheets.raspberrypi.com/